# Methods
## Encoder
-encoder architecture is inspired by yin2015abc but instead of a final classification task on both inputs we pass the vectors to a decoder which is supposed to reconstruct a simple English sentence out of it
### BCNN
- models two sentences in parallel by two CNNs with shared weights (siamese architecture)
- final layer connects the two CNNs and solves the given task
- input: word2vec embeddings of sentence → feature map of dimension d0 x s
- wide convolution such that the “outer” words can be detected by the “inner” weights
-average pooling (all-ap):
-applied to feature map of last convolution layer
- column-wise averaging over all columns (all-ap)
-results in representation vector which then can be passed over to classifier etc.
-average pooling (w-ap):
- column-wise averaging over a window of w consecutive columns (w-ap)
- is applied to every non-final convolution layer

- output layer: input from last convolution layer and all-ap applied, but it also recieves a representation of each non-final convolution layer. Normally, w-ap is applied and the output is given to the next layer but here all-ap is also performed in parallel and the output is directly forwarded to the output layer. This potentially boosts the performance as different levels of abstraction are accessed in the output layer.
### Modifications to the network
- 4 convolution layers
-no task specific final layer as we want to use the trained encoder to produce inputs for the decoder
-instead trained encoder with loss function such that the similarity of the representation of a simple and a complex sentence is maximized if they are labeled 1 and minimized if labeled 0
-started with L2-norm (euclidean distance) and then switched to cosine similarity as our End2End model did not learn anything

## Decoder
- architecture mirrors the one from the encoder but with k-nearest-neighbor interpolation/upsampling
- loss: first L2 than cosine similarity of word embedding of input sentence and corresponding simple sentences
### Transposed Convolution

## End2End Approach
-alternative to sequential training of encoder and decoder
- input only word embedding of complex sentences and the gold standard is the word embedding of the simple sentence (no sentence pairs anymore)
- loss: first L2 than cosine similarity
- did not learn anything and hard to debug
- stopped end2end approach and focused on separate training

# Results

# Discussion
Data set is noisy!
Additional information (co-reference)
Simple sentence 1.5 times the length of complex one
sometimes not really simplified matches
Maybe train word embeddings on our corpus
Encoder: very similar representation for simple and complex sentence
Decoder: cannot reproduce word embedding of simple sentence from feature map of complex one
End-to-end: cannot produce simple embedding from complex one

# Summary and Outlook